## Slide 1: Week 4: Presentation & Final Report
Final report covering VLAN setup, FortiGate integration, trunking, and testing results.

## Slide 2: Objective of Week 4
• Consolidate all project findings
• Prepare final written report
• Prepare presentation summarizing configuration steps
• Include VLAN setup, FortiGate integration, testing results

## Slide 3: VLAN Setup Summary
• DMZ Zone:
- VLAN 100 (Linux1)
- VLAN 200 (Linux2)
• TRUST Zone:
- VLAN 10 (Win1)
- VLAN 20 (Win2)
• Access & trunk ports configured on both switches

## Slide 4: FortiGate Integration Steps
• Created sub‑interfaces:
- port2.100 → 192.168.100.1
- port2.200 → 192.168.200.1
- port3.10 → 172.16.10.1
- port3.20 → 172.16.20.1
• Configured gateways
• Added firewall policies between all VLANs

## Slide 5: Firewall Policies Included
• VLAN 10 ↔ VLAN 20
• VLAN 10/20 ↔ VLAN 100/200
• VLAN 100 ↔ VLAN 200 blocked by design
• Internet access allowed for all VLANs (if applicable)

## Slide 6: Testing Results
• VLAN 10 → VLAN 20: Success
• VLAN 10 → VLAN 100/200: Success
• VLAN 20 → VLAN 10: Success
• VLAN 20 → VLAN 100/200: Success
• VLAN 100 ↔ VLAN 200: Fail (Expected)
• All results match expected behavior

## Slide 7: Final Report Contents
• Complete documentation of:
- VLAN creation
- Access/trunk configuration
- FortiGate sub‑interfaces
- Firewall rules
- Testing table and screenshots
• Added conclusions and observations

## Slide 8: Conclusion
• VLAN segmentation fully implemented
• FortiGate routing and security working correctly
• Network achieved isolation + controlled communication
• All tests validated successfully